## Slide 1: Ecal Resolution Studies and update
Jason Barkeloo
J. Brau, A. Steinhebel, E. Meyer, J. Carlson
University of Oregon
ALCW 2018
June 1, 2018

## Slide 2: Outline
KPiX
Reminder of What Has Been Done
  Where I started on the project
    Test Beam Simulation and Comparison to KPiX data
    How we start applying these to the full detector model
Current Geometry Studies
  Effects on Resolution
Beginning to Look at Simulated Events

## Slide 3: Particle flow Calorimetry
SiD has been designed to use Particle Flow Calorimetry to measure all final states with precision
We expect excellent jet energy resolution
  Measure charged momenta with tracker, neutral energies with calorimeters
  Requires very fine segmentation
An “Imaging ECAL” is a crucial part of the design
  Silicon-Tungsten based calorimeter is being developed for a high granularity ECAL
  KPiX ASIC for readout of silicon pixels

## Slide 4: kpix
6 inch wafers
1024 13mm2 pixels
Readout and cable are bump-bonded directly to the sensor
Test beam studies have happened with an initial version of this KPiX sensor design
Will come back to the geometry and its effect on resolution measurements

## Slide 5: Test beam studies
Small 9 layer stack was placed into SLAC test beam
Sensor issues have been found and change the design going forward
  Cross Talk, Dead Pixels, …
Many electron events were seen that we can analyze and compare with simulation to improve understanding of the system
  Resolution, Identification (how well we can tell how many electrons are in an event)

## Slide 6
Geant4 Simulation created of 40x40cm plane of alternating Si (320 μm) and W (2.5mm,5/7 χ0 )
  40 (thin W) layer detector simulated simulated, only include 9 to match test beam stack for comparisons sake
  Electrons fired at origin of various energies (in particular 12.1 GeV, test beam energy)
  Want to try to match test beam running conditions
1000events, 10GeV. Energy in MeV deposited (all events summed) on the z-axis.

## Slide 7: Comparisons (cont.)
  Attempted to model distribution of electron multiplicity and errors in test beam
    10% pixels randomly removed from each layer
    Poisson distribution of simultaneous electrons per event used <n>=0.8725
    Shifted from central area (more densely pixelated, also test beam was shifted away)
    Match hit to KPiX pixel location

## Slide 8: Comparisons (cont.)
Excellent agreement to test beam data.
Couldn’t remove all of the low E shoulder during test beam cleaning (lots of ~0fC hits)

## Slide 9: Counting Electrons
Algorithm used to count the number of electrons in the even based on energy distributions throughout the detector.

## Slide 10: Counting Electrons (Cont.)
No field, just simple detector simulation

## Slide 11: ECAL Geometry And its Effects
20 layers 2.5mm W
10 layers 5mm W
30 gaps 1.25mm w/pixel sensors
29 χ 0

## Slide 12: Geometry Effects
Leakage into HCAL in overlap region increases due to less material, phi dependent

## Slide 13: Resolution Effects from geometry
Previous resolution study (Da An, et al. 2014) using 100 GeV photons in sidloi3.
 Resolution ~
 Resolution ~
Resolution study using 10, 50, 75, 100, 250, and 500 GeV electrons using Simple Geant4 Stack Simulation
For lower energy e- (<100 GeV), Resolution much closer to design expectation (17%/)
E. Meyer

## Slide 14: Distrubutions
Use cone width ± 0.2 rad constraint on hit locations (avoid backscatter)
  determined from incident MC particle, not actual hits in detector
  Ignore 5 GeV electrons in resolution plots, B-field effects  shower gets missed with constraint
5 GeV
10 GeV
50 GeV
100 GeV

## Slide 15: Comparisons
Discrepancies
SiD resolution degrades much faster than the simple stack resolution
100 GeV SiD photons for have Res ~ compared to ~ from previous sidloi3 study
100 GeV SiD photons have slightly better resolution than previous sidloi3 study; compared to ~

## Slide 16: Confirm simple stack behaves as expected
Vary the number of thin and thick layers for simple stack electrons
#Thick Layers = (40 - #Thin) / 2
Expected resolution of 40 thin ~
  measured
Expected resolution of 0 thin layers to degrade by (~)
  measured
Conclusion: simple stack behaves as expected
*Note: Simple stack absorbers are pure W

## Slide 17: sidloi3 results
Previous study
(Da An, et al.)
Current study 
(what is used on following resolution plot)
Small/negligible difference between and
Large difference between and

## Slide 18: SIDloi3 Results (cont.)
Consistency
Resolution at for old and current sidloi3 studies match
Discrepancy
For , old and current studies do not match ( compared to )

## Slide 19: How does incident hit location in module affect resolution?

## Slide 20: Resolution Dependence on phi
Closest overlap region to normal incidence: ~
ensures entire shower goes through center of module
100 GeV e- at is comparable to simple stack
flipped from diagram on the right

## Slide 21: Summary of current Resolution results
Current SiD compares better to previous studies when incident particles are fired at instead of normal incidence
Shower mostly contained in nonoverlapping region
Next: What about real events?!

## Slide 22
  Calo hits
  Truth MCParticle
  Electron/Positron
Pandora PFOs

## Slide 23: Investigation of photon-photon opening angle
  Raw Data
  Truth Info
  Pandora PFOs

## Slide 24: Truth Energy Resolution around True Rho
Choosing a certain percent of the rho energy and looking at the percent of events that contain that amount of the rho energy vs. the cone angle.
0.05rad → ~6cm
~<20 pixel widths
Choosing a certain cone angle and looking at the cumulative distribution for how many events get to a certain percent of the rho energy shown on the x-axis.

## Slide 25: Summary
Better understanding current results more every day
  Resolution differences from initial design resolution to current design geometry
  Comparison between versions of geometry can be tricky
Initial π0→γγ resolution studies underway

## Slide 26: Backup

## Slide 27: W-First vs Si-First simulation
Distribution of energies in simulation depending on which way the test beam was facing into the detector, small differences

## Slide 30: BackScatter